## Slide 1
Assembly Instructions
last updated
October 2012

## Slide 2
[NOTE: It is easier to assemble your Earthmaker on a non-skid surface. The Earthmaker can then be picked up and moved to its final site.]
Stand the FRONT PANEL on a flat, level surface (NB: see User Guide - Site Selection).
Stand a SIDE PANEL at right-angles to the front panel.
Step
1

## Slide 3
Pull the corner tabs together so they overlap.
Slide the CONNECTOR STRIP between the tabs – pointed end down.
Use the handle at the bottom of the connector strip to guide it through.
Step
2

## Slide 4
Stand the other SIDE PANEL at right-angles to the other side of the front panel.
Pull the corner tabs together so they overlap.
Slide another connector strip between the tabs.
Step
3

## Slide 5
Fit a SHELF to the front and side panels at the lower position. NB: Ensure the lugs are aligned with the slots.
Push the lugs at the front of the shelf into the slots in the side panels – work from the front to the back of the shelf.
Push lugs at the back of the shelf into place.
HINT 1: Lubricating the lugs, and slots (eg: with silicone spray) can assist assembly.
Step
4

## Slide 6
HINT 2: Use the heel of your hand to push the lugs into place
Step
4 - continued

## Slide 7
When the lower shelf is secure, place the BACK PANEL between the two side panels.
Pull the tabs together and slide the connector strips between them.
Step
5

## Slide 8
Fit the other SHELF to the back panel and the two side panels - pushing the lugs into the slots.
NOTE: This upper shelf slopes down from the back panel towards the front, while the lower shelf slopes down from the front panel towards the back
Step
6

## Slide 9
Fit the LID to the TOP in the fully open position.
Align the lug on the spindle with the notch in the hole.
Push the spindle firmly into place. (It may help to place the assembly upside down on a soft surface and apply pressure with a foot.
Check from to ensure the spindle is fully in place.
Step
7

## Slide 10
Fit the TOP PANEL.
Starting with the back and sides, snap the slots over the tabs. Support the side panels from the inside while pushing the top panel down to make a definite click.
Snap the slots at the front over the tabs on the Front Panel while pushing the front panel out from the inside.
Step
8

## Slide 11
Insert the PULL-OUT PANEL into the slot above the door.
Check that the DOOR is correctly fitted.
Place the door in the front panel so that its bottom edge fits behind the rim.
Step
9

## Slide 12
Position the Earthmaker, so that it is:
conveniently positioned in relation to your kitchen
on a flat, level, well drained surface (eg: paving slabs)
shaded from very hot sun
suitably positioned for extracting mature compost.
CHECK that the top is properly in place after moving.
Step
10

## Slide 13
Hang the PUSH-PULL-TOOL on a hook at the top of one of the connector strips.
Your Earthmaker is now ready for use - read the User Guide.
Step
11

## Slide 14
thank you